## Slide 1: Energy-Efficient Computing: Do We Have A Roadmap?
Peter Kogge
McCourtney Prof. of CSE, Univ. of Notre Dame
IBM Fellow (retired)
Cray, IEEE Computer Pioneer Awardee

## Slide 2: Computing Has Reached the “Cambrian Explosion”
Cellular Automata
Map Reduce
Systolic Arrays
Petri Nets
Actor model
Lambda Calculus
Combinators
Logic Computing
Reversible
Probabilistic
Functional
Data Flow
Neural Morphic
Adiabatic
Analog-Electrical
Analog-Mechanical
Genetic
Ising
DNA
Fluidics
Optical
Quantum
Coupled with growing irregularity, sparsity, transitory computation,
what “consumes” power is changing!

## Slide 3: What is Energy-Efficient Computing?
We Don’t Mean Just:
  Lower energy/flop
  Lower node power
  Lower energy per computation
We Do Mean:
  Lower Overall Energy At Performance Comparable or Better Than What Is Achievable Today
  At the Same Size Problems, Or Bigger
Will Require ATSAA:
  Architecture/Technology/Software/Algorithm/Application Codesign
Particularly Science specific

## Slide 4: First Observation: Evolution of Challenges
2000: DOE Report “Scientific Discovery through Adv. Computing”
  Beginning of ubiquitous parallelism
  Challenge: Make full use of terascale
  Critical issues: performance, portability, adaptability
    Sim codes 5%-10% of peak – and decreases with parallelism
2008 Exascale Study: Need much tighter tie-in to architecture
  Design for energy
E,g. Computing energy of Iso-octane
275M nonlinear equations
Iterative solution
2.5PB between processors
15 TB to disk
30 PFlops

## Slide 5: The 2008 Exascale Eye-Openers
Energy/Power was the dominant factor
Only path forward
  Simpler chips at less than max clock rates but massive parallelism needed
  Alternative packaging
  High degree networks
  Must deal with greatly reduced memory bandwidth per op
Dongarra, J., Keyes, D. The co-evolution of computational physics and high-performance computing. Nat Rev Phys (2024). https://doi.org/10.1038/s42254-024-00750-z

## Slide 6: Topics
The Road to Exascale: Lessons Learned
Deep Dive on The Past
Technology Advances
Projections to Zettascale
Non-Obvious Research Directions

## Slide 7: Review: The Road to Exascale
Includes content from “Frontier vs the Exascale Report: Why so long? and Are We Really There Yet?” by Kogge & Dally, SC 2022

## Slide 8: The HPL World in 2008
Roadrunner: 1+ PF/s
DARPA (Bill Harrod): Exa by 2015?
2008 Exascale Report: Yes, but…
Roadrunner
ASCI Red
Exa Goal
*
“First Light” for new TOP500 entries
1015 Flops/s
1018 Flops/s

## Slide 9: The HPL World in 2022
2022: Frontier Cracks 1EF/s
  7 years after Report Goal
  4 years after extrapolating curve
Bounding Curve Changed in 2013
Roadrunner
ASCI Red
Exa Goal
*
Frontier
*
Obvious Questions
What Is/Was Exascale?
What Did 2008 Report Predict?
Comparison to Frontier
What did Report get Right/Wrong?
“First Light” for new TOP500 entries
1015 Flops/s
1018 Flops/s

## Slide 10: The Exascale Study Report Outline
What should “Exascale” Mean?
The 2008 state of the art
  Architectures, Runtimes, Programming, Metrics
2008 Application Characteristics
  Computation vs Memory intensive Apps, Scaling, Concurrency
Technology Roadmaps
  Logic: Silicon and Non, Memory, Storage, Interconnect, Packaging, Resiliency, Programming Models
Strawman Designs
  Subsystem projections, Evolutionary designs (Heavy and lightweight), Aggressive design
Challenges & Research Areas
  Power, power, power, & power
  Memory capacity & bandwidth
  Programmability
  Reliability
Blue: Addressed here
Practically Solved
Remain

## Slide 11: What Was Exascale?
Report Emphasis: Try to change focus from flops
Goal: overall 1000x capability over “Petascale” by 2015
  In Same Footprint for Supercomputer at max 20MW
  1000X in a rack (peta scale)
  1000X in a module (tera scale)
Goal: not just flops but 1000x in:
  Memory
  Memory Bandwidth
  Network Bandwidth
  …
Plus ability to efficiently use massive concurrency

## Slide 12: Technologies Investigated
Logic: power, area, energy, clock
  CMOS: hi perf/low voltage
  Options: hybrid, superconducting
  Voltage scaling
Main Memory
  SRAM, DRAM, NAND, Alternatives
  Reliability, packaging, power
Storage Memory
  Disk, Holographical, Archival
Interconnect: esp. energy
  On chip
  DRAM to Processor (Stacking)
  Intra/inter module
  Rack to rack
  Electrical vs optical
Packaging and Cooling
Resiliency & Checkpointing
Programming Models

## Slide 13: 2015 Aggressive Strawman Design (2013 Tech)
Node: 742 simple cores/chip with 4 FPUs @ 1.5GHz
32nm CMOS with 30Gb/s SERDES
16 Memory channels: each 1 GB Stacked DRAM
150 Watts w’o routing chip
Group: 12 nodes with 12 64-radix router chips
Includes 16 12GB SATA drives for checkpointing
Cabinet: 32 Groups = 384 nodes
Assumed max power of 120KW
System: 583 Cabinets, 67MW
3-hop Dragonfly interconnect (optical)
166 million cores with 664 million FPUs
Est. 14.9 GF/W
Or 67 pJ/flop
WD

## Slide 14: Power/Energy Constrained Memory Bandwidth
Chart: 
| Register file | L1 | L2 | L3 | Local DRAM | Global DRAM
Flops/Byte accessed | 1 | 4 | 8 | 16 | 50 | 164
Need to do 164 flops
For each byte of remote
Memory accessed

## Slide 15: Where Did the Energy Go?

## Slide 16: 2022 Frontier Node
Heterogeneous Processors
  64-core 2GHz CPUs
  Quad GPUs: closer to Strawman
    But more FPUs/core
    And slightly faster
Chiplet design
Mixed memory hierarchy
  8 DDR4 DRAM Channels
  8 HBM2e stacks/GPU
Quad network ports
Measured 52.2 GF/W
~3.3X Strawman
PMK

## Slide 17: Frontier vs Strawman
Strawman’s huge #s of nodes
  Exploded # of Network ports
  And thus huge switching costs
Frontier had fewer, bigger nodes
  Reduced network ports
Comparable Memory Bandwidth
  Use of wide stacked memory
  But only 3X capacity
Essentially same N/W topology
  But 2X better SERDES
  And 2+X better bisection B/W
WD

## Slide 18: Frontier vs Roadrunner: Did We Get 1000X?
Flops/s exceeded 1000X / cabinet
  But huge cabinets
  Within 3X for chip & node
Only ~100X in flops/s per watt
  And flops/cycle
Miserable increase in Memory, Memory Bandwidth. N/W Injection Bandwidth

## Slide 19: Report Card
What We Got Right
CMOS, flat clocks
Large # of wide simple cores
Aggressive memory hierarchy
Stacked memory
Near reticle-limited dies
Energy of movement predominates
Near billion-way concurrency
Memory concerns were valid
Dragonfly with hi radix switches
N/W signaling rate would improve
What We Missed
Heterogeneous designs
SIMD width much larger
Stacked memory: more ports/lower transfer rate
Machine Learning & short FP
Massive 500W chips
Reliability not a show-stopper
New programming models

## Slide 20: What about “Zettascale”

## Slide 21: Industry Projections: Road to 1 Zettaflops/s
2018: China NUDT: 2035 is reasonable
  Moving from exascale to zettascale computing: challenges and techniques. Frontiers Inf Technol Electronic Eng 19, 1236–1244 (2018). https://doi.org/10.1631/FITEE.1800494
2021: Intel: 2027 may be possible
  Raja’s chip notes lay out intel’s path to zettascale. https://www. servethehome.com/rajas-chip-notes-lay-out-intels-path-to-zettascale/, 2021
2023: AMD: 2035 is reasonable
  https://www.hpcwire.com/2023/02/21/a-zettascale-computer-today-would-need-21-nuclear-power-plants/
All assume power budget 50-100MW

## Slide 22: NUDT’s 2018 Projection for 2035
Technical Challenges: Manufacturing, Energy, Interconnect, Storage, Reliability, Programming
Expected changes
  Architecture: heterogeneous, mixed precision, near-memory, non-von Neumann
  Package driven: 3D integration, inter-chip interconnection,density per node to 0.5-0.8 Pflops/s @0.8 Tflops/W
  Network: electrical to exceed 50Gb/s, optical CWDM to 112Gb/s per channel, on-die photonics
  Storage: 3D stacks, hybrid multi-layer storage, NVM, Network attached memory
  New technologies: memrister, quantum
  Programming: MPI+X, with variety of intra-node threading models, DSLs
100,000 Nodes
1000W per node
Only 1.5X more floor space implies100KW per sq. m of floorspace, or 3.2X more power per rack

## Slide 23: Intel 2021: Zettaflops/s by 2027-28
Goal: same power as ~2Eflops Aurora
Architecture: 16X – “AI Math” + keeping execution units fed from memory
Power/Thermals: 2X – Lower voltages and higher-end cooling (eg liquid cooling but more than rear door heat exchangers
Data Movement: 3X – higher integration, fewer better SERDES
Process: 5X - multi-tile design with advanced packaging that allows technology mix
Phase 1: 2022-23 Exascale+
  “Granite Rapids”
Phase 2: 2024-25 Pre-Zetta
  “Falcon” = Xeon + Xe
  “Lightbender” = Silicon photonics
Phase 3: 2026-28: Zetta
  Reduce 50MW Exaflop-class to 50KW
  Requires all changes from left

## Slide 24: AMD: Need to Use “AI”
https://www.hpcwire.com/2023/02/21/a-zettascale-computer-today-would-need-21-nuclear-power-plants/
1
4
2
Missing 5X
3
-3X-
-3X-
-5X-
-5X-

## Slide 25: Clear Takeaways
Focus seems to solely be on flops/s
Energy efficiency the major challenge
Power budgets of 100MW imply need 200X in efficiency
No silver bullet from “traditional” architecture
Process improvements small (3X?)
Bulk of improvement riding on packaging, esp. 3D
Much hope on “AI” – i.e. mixed precision
Memory/networks mentioned but not any real thought

## Slide 26: Deep Dive on The Past: An Energy Focus

## Slide 27: The Multi-Faceted World of 2020s
“First Light”: 1st appearance
Color=Benchmark
  HPL
  HPCG
  HPL_MxP
  BFS
  SSSP
Fill
  Solid: with GPUs
  Hollow: without

## Slide 28
CAGR
HPL: 1.2
HPCG: 1.13
BFS: Flat
HPL
HPCG
HPL_MxP
BFS
SSSP
10X in 12 years
5X in 12 years

## Slide 29
Seems to have been ~ constant since ~2018
“System” power/core >> chip power per core
We need to look at “system”

## Slide 30: Today’s Node Design – Energy of Movement
Processor Chiplet
On-chip Network
Chip-chip to cache die
Chip-substrate to IO die
Processor Chiplet
On-chip Network
Chip-chip to cache die
Chip-substrate to IO die
Processor Chiplet
On-chip Network
Chip-chip to cache die
Chip-substrate to IO die
Processor Chiplet
On-chip Network
Chip-chip to cache die
Chip-substrate to IO die
Processor Chiplet
On-chip Network
Chip-chip to cache die
Chip-substrate to IO die
Processor Chiplet
On-chip Network
Chip-chip to cache die
Chip-substrate to IO die
Processor Chiplet:
On-chip Network
Chip-chip to cache die
Chip-substrate to IO die
IO Chiplet:
Chip-substrate to Proc die
On-chip networks
Chip-substrate to HBM
Chip-module-PC card to GPU
Chip-module-PC card to DRAM
Chip-module-PC card to NIC
GPU Module:
PC card to Proc Module
Substrate to GPU chip
On-GPU chip networks
Chip-substrate to HBM
DRAM PC Card:
PC card to DRAM Die
Chip-Chip to stacked DRAM
NIC Module:
PC-card to Module
On-chip networks
Chip-substrate to HBM
Chip to Network
HBM Stack:
Substrate to GPU
Chip-chip to memory die
Switch Module:
Chip to Network
On-chip networks
Lots of On & off chip
Networks/crossbars
Processor Module
Same colors = similar functions

## Slide 31: Technology Advances
A Quick Subset

## Slide 32: Lower Operating Voltage – No Free Lunch
Lower voltage implies lower energy per operation (good)
Implies lower clock rates
Implies more parallelism needed
Requires more paths for interconnect
And more data movement
And more power spent in data movement (bad)

## Slide 33: And What About Memory?
Assume characteristics scale as they did from Peta to Exa
Relative capacity dropping
  Can problem size scale with flops?
Is being able to access a word of memory every 400 flops acceptable?
With all the deep cache hierarchies how much extra data transfers between memories are there?
  All of which consume power
 | Petaflops/s | Exaflops/s | Zflops/s
 | Roadrunner | Frontier | At same ratio
Capacity (Bytes) | 0.036PB | 0.009EB | 0.0025ZB
Bytes per flops/s | 0.032 | 0.0075 | 0.0025
Bandwidth (Bytes/s) | 0.378PB/s | 0.125EB/s | 0.04ZB/s
Bandwidth per flops/s | 0.344 | 0.105 | 0.04
Flops per Byte | 3 | 10 | 25

## Slide 34: At Best Modest Gains in PHY/SERDES Energy
 | 2008 Projection | Recent |  | 
Data Movement | Energy | Bandwidth | Energy | Citation
Chip-chip vertically on Thru Silicon Via | 0.01pJ/b |  |  | 
Long range on chip | 0.018pJ/b/mm |  |  | 
Chip-chip copper | 2pJ/b | 224Gb/s | 3pJ/b | ISSCC 2024 Paper 7.3
Routed Interconnect | 2pJ.b + 1pJ/b per switch |  |  | 
Optical | 1.5pJ/b + 0.1pJ/bit for routing | 224Gb/s | 1.04pJ/b | ISSCC 2024 Paper 7.2

## Slide 35: My Thoughts
Need to consider more than HPL
Solution has to be heterogeneous & hybrid
  Integration of “AI” beyond just mixed precision
  Need to seriously reconsider “Probabilistic” algorithms
More specialized computation will move:
  Closer to CPUs on die/module
  Further from CPUs into memory and network
Levels of parallelism will seriously explode
  Places more stress on networking
  We cannot afford deep S/W stacks to start computations “over there”
Memory system given short shrift

## Slide 36: Stacking: Reduce Die-Die Energy Cost
Modern HBM
AMD 3D Stacked V-Cache
2011 MICRON HMC
https://scx2.b-cdn.net/gfx/news/2021/benefits-of-3d-soc-des.jpg
1990s Irving Sensors Die Stack
Apple 2012 iphone chip stack
2008 Exascale Strawman

## Slide 37: Chiplets
Chiplet: Breaking large tiled die into multiple smaller die
  And place on substrate not PC
  With lower energy per bit transferred
Reason: Increase yield => Lower cost
  Also promote “mix & match”
Side-effect: Increased off-die contacts
  Each will consume energy
AMD Genoa 12x16C Chiplets
Torus
1D
Mesh
1 die/system
16 die/system
I/O &
Memory
Chiplet
Silicon Interposer

## Slide 38: ISSCC 2024 – New Architectures Sessions & Forums
15: Embedded Memories & Ising Computing
17: Emerging Sensing and Computing Technologies
20: Machine Learning Accelerators
29: ICs for Quantum Technologies
30: Domain-Specific Computing and Digital Accelerators
34: Compute-In-Memory
F1: Efficient Chiplets and Die-to-Die Communications
F2: Energy-Efficient AI-Computing Systems for Large-Language Models
F3: Digitally Enhanced Analog Circuits

## Slide 39: Examples of Novel In-Memory Accelerators
SRAM ISING In-memory Optimizer (ISSCC 2024 15.5)
Post Quantum Crypto-processor (ISSCC 2024 16.2)
74TF/s BF16 Compute-In-Memory for Diffusion Models (ISSCC 2024 20.2)
Compute-In-Memory PINN
(ISSCC 2024 20.4)
Compute-In-Memory Spiking Neural Net
(ISSCC 2024 30.2)
Compute-In-Memory SAT Solver
(ISSCC 2024 30.3)
In-Memory Annealing Processor
(ISSCC 2024 30.4)
Compute-in-Memory with 31.2TFLOPS/W(ISSCC 2024 34.8)

## Slide 40: Spiking Neural Net Accelerators
IMEC
Intel
Renesas 8.8TOPS/W
BrainScale S-2 Chip
Cerebras Trillion Transistor Chip
IBM TrueNorth CHip

## Slide 41: Diving into Cross Node Communication Costs in Parallel Codes - and Their Energy Impact

## Slide 42: Example Effects of Imperfect Parallel Scaling
Underlying Problem: Growing Transient Computation

## Slide 43: Amdahl Model and a Time-Energy Trajectory
Time = A + B/N (N= # nodes)
  A = single node serial time
  B = single node parallelizable time
  Asymptotic speedup = (A+B)/A
B = 0 is “No parallelism”
A = 0 is “Perfectly Parallelizable”
Each line: Same A,B values but with different # of nodes
  (1,1): time with a single node
  Large marker = 128 nodes
  Red line: more nodes just cost energy
  Blue line: more nodes speeds up perfectly
No parallelism
No serial component
Some serial
component
A+B/A=1
A+B/A =3
A+B/A =10
A+B/A =100
A = 0
No parallelism
Perfectly Parallelizable
Some serial
component
A+B/A=1
A+B/A =3
A+B/A =10
A+B/A =100
A = 0

## Slide 44: A “Cost of Communication” Model
Chart: Node Count
| 1 | 2 | 4 | 8 | 16 | 32 | 64 | 128
0 | 1 | 0.5 | 0.25 | 0.125 | 0.0625 | 0.03125 | 0.015625 | 0.0078125
0.25 | 1 | 0.625 | 0.4375 | 0.34375 | 0.29688 | 0.27344 | 0.26172 | 0.25586
1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
2 | 1 | 1.5 | 1.75 | 1.875 | 1.9375 | 1.9688 | 1.9844 | 1.9922
5 | 1 | 3 | 4 | 4.5 | 4.75 | 4.875 | 4.9375 | 4.9688
Assume a “graph-like’’ model
Multiple edges must be followed
  Equally partitioned among all nodes
  Compute cost/edge = T
  Cost if edge goes off node = C
C/T = 1 is a critical parameter
  C/T<1: some speedup
  C/T > 1: more nodes counter-productive
Each line: Same C/T values but with different # of nodes
  (1,1): time with a single node
  Large marker = 128 nodes
  Lines with C/T≥1 get worse in energy AND time
  Lines with C/T<1: more nodes speed up
No parallelism
No serial component
Some serial
component
C/T = 5
C/T = 2
C/T =1
C/T=0.25
C/T = 0
C/T = 5
C/T = 2
C/T =1
C/T=0.25
C/T = 0
Code gets slower
With more nodes
Communication has NO cost

## Slide 45: Looking at Such Trajectory Graphs Can Help Id Properties of Code
C/T = 5
C/T = 2
C/T =1
C/T=0.25
C/T = 0
Code gets slower
With more nodes
Communication has NO cost
No parallelism
Perfectly Parallelizable
Some serial
component
A+B/A=1
A+B/A =3
A+B/A =10
A+B/A =100
A = 0
Curves like this imply an Amdahl Model
Curves like this imply a Communication Model

## Slide 46: Example: Subgraph Isomorphism
Find instances of complex subgraph in a very large graph
Multiple parallel implementations
Mig. Threads need no comm s/w
Takeaway: Best of conventional must use 87+% of its cycles in handling inter-node comm
We’ve seen similar results in ML, SpMV, …
Cilk on Single Node
Modern Multi-core, Multi-n0de
Migrating Threads
13,300
3560
466
See Kogge, McMahon, Dysart, HPEC 2024

## Slide 47: An Example of A New Architectural Technique
Migratory Threading
All memory on a single logical space
On nonlocal reference: H/W
  Suspends thread
  Packages State
  Sends to correct node
  Unpacks State
  Restarts thread
Cheap spawns
32 node Lucata Pathfinder
at GaTech’s Rogue’s Gallery

## Slide 48: Actual Performance/Energy Trajectories
Chart: Time (s)
| 8.31 | 4.38 | 2.63 | 1.4 | 1.81
SHAD-1:1-16N@78ME | 2908.5 | 3066 | 3682 | 3920 | 10136
SHAD-1:1-16N@38ME | 875 | 952 | 1064 | 1960 | 5600
SHAD-2:1-16N@78ME | 1555.7982 | 1640.0472 | 1969.5544 | 2096.864 | 5421.8912
SHAD-2:1-16N@38ME | 468.05 | 509.2384 | 569.1488 | 1048.432 | 2995.52
OPENCILK:1N@79ME | 8136
Prolog-1:1C@2ME | 5.115
Prolog-2:1C@2ME | 12.22
Prolog-3:1C@2ME | 42.2933
Python:1C@3.4ME | 182.6381
MT:1-32N@38ME | 96.8481 | 130.4226 | 147.4981 | 234.6993 | 437.9039 | 856.1095
MT:1-32N@78ME | 187.65 | 268.6944 | 298.5978 | 419.9212 | 714.9551 | 1181.4451
Scaled Prolog | 91.9855 | 219.7581 | 760.5814
Joules = Power * Time
Each Curve: same dataset but different nodes
Closer to Origin is better
Solid Curves: 78M Edges
Dashed Curves: 38M Edges
Red Lines: Modern 128 core 2.8GHz nodes
Green Lines: Older Cluster with 3 GHz cores
Blue lines: Pathfinder (CRNCH resident) Migrating Thread system with 180MHz
Conventional Systems Appear to have Communication Model characteristics
Migrating Threads far more scalable
  At higher performance per clock
Prolog on 1 laptop core
But smaller dataset
Cilk on 1 node
Puma

## Slide 49: My Suggested Research Directions

## Slide 50: Three Major Research Components
Promote “Benchmarking for Understanding”
Architect to reduce inefficiencies due to “border crossings”
Develop flexible “hybrid” algorithmic techniques

## Slide 51: #1: Benchmarking for Understanding
Reasons for Benchmarking
Competitive benchmarking: “my system is better than yours”
Technical benchmarking: “I get best performance with parameters xyz”
Projective benchmarking: “by looking at previous generations the next Moore’s Law increment tech level should increase performance by X”
Benchmarking “Crimes”
Selective benchmarking,
Using wrong benchmarks,
Improper comparison of results,
Improper interpretation of results,
Measurement omissions
See G. Heiser, “Systems benchmarking crimes,” https://gernot-heiser.org/benchmarking-crimes.html
Today
Internal

## Slide 52: Current Benchmarks (From Upcoming Paper)
Inadequate for
“Understanding”

## Slide 53: The Benchmarking Bridge
Goal: Institutionalize process:
To enable deep understanding how computational infrastructure affects performance
As a function of benchmark characteristics

## Slide 54: We Need to Capture Cross-Benchmark Data

## Slide 55: Expanding Scalability Studies beyond Kernels
Define kernels and WORKFLOWS:
  Compositions of kernels
  With multiple data set sizes
  To be measured over multiple system sizes
Example: AGILE program from IARPA
  Workflow 1: Knowledge Graphs – Groups, Relationships, and Interests
  Workflow 2: Detection – System and Event Patterns
  Workflow 3: Sequence Data – Identification and Clustering
  Workflow 4: Network of Networks – such as Cyber-Physical Systems
Each with several variations
Include instrumentation to track major energy-costly events
i.e. Not just the highest performance but how does app/infrastructure scale – both strong and weak

## Slide 56: #2: “Border Crossings”: The New Bottleneck
General
Purpose
Socket
DDRx
DDRx
General
Purpose
Socket
DDRx
DDRx
.
.
.
.
.
.
General
Purpose
Socket
DDRx
DDRx
General
Purpose
Socket
DDRx
DDRx
.
.
.
.
.
.
Network Interface Chip
GPU
Socket
GDDR
GDDR
.
.
.
GPU
Socket
GDDR
GDDR
.
.
.
HBM
HBM
HBM
HBM
HBM
HBM
Today
Tomorrow
Near/In Memory
Accelerators
At least three kinds of computational “crossings”
Physical separation of computational units
Change in ISA/Execution model
Significantly different engine technologies

## Slide 57: #3: Innovation in “Hybrid” Algorithms
Hardware is going heterogeneous
  Codes will bounce between different “cores”
Algorithms are rapidly involving new models of computation
  AI, Quantum, Analog in Memory…
We need to understand algorithms that do both
  EFFICIENTLY without wasting processing cycles

## Slide 58: History (and Future) of Algorithms
As we move down
Solutions get faster
Likely to be more hybrid, heterogeneous
“Accuracy” becomes less well-defined
Need to understand “costs” of hybridization
Technique | Repeatable Results | Bounded Precision | Execution Time
Direct Solvers | Yes | Within roundoff | Predictable
Iterative Solvers | Yes with same seed | Usually testable | Iterative improvement
Monte Carlo | Yes with same seed | Math bounds | Iterative improvement
ML-based | Yes | Weak | Fixed (Inferencing)
Quantum | No | Distribution | Needs multiple runs
Classical
Analog/AI/Quantum
Run
Parameters
Result
Measurements

## Slide 59: ML/AI Discussion
Use as universal function approximators
  Learning: Discover equation (learn from solvers or experimental data)
  Inferencing: Replace conventional solvers
PINNs: Physics Inspired Neural Nets
  Designed with classes of ODEs/PDEs in mind
  Train to find coefficients
Techniques exist to architect NN for dynamically adjustable time/accuracy
See for example: https://towardsdatascience.com/solving-differential-equations-with-neural-networks-afdcf7b8bcc4
Also “Physics-informed neural networks: A deep learning framework for solving forward and inverse problems involving nonlinear partial differential equations.” Journal of Computational physics (2019)
“A hands-on introduction to Physics-Informed Neural Networks for solving partial differential equations with benchmark tests taken from astrophysics and plasma physics”, https://arxiv.org/pdf/2403.00599v1
Example of Solovlev Equilibrium

## Slide 60: Summary: My Suggested Research Directions
Much of new technology will be researched by industry
  Rapid escalation in heterogeneity
Research focus should be on improving energy efficiency for Science apps using alternative models
Understand where are energy-inefficient events
Develop architectures that avoid inefficient border crossings
Design algorithmic techniques that reflect changing nature of computing
Understand
Benchmark
Results
Architect around
Inefficient Changes to
sites of computation
Develop algorithmic
Techniques to
Leverage new
Computational models
Codesign to
“Right-Size”
Node Designs

## Slide 61: Apps using just Migrating Threads
Sparsest of SpMV Cases
Firehose Streaming
ML SGD SVM
Far better scaling on sparsest cases

## Slide 62: Possible Growth to Interfacing Heterogeneous System
Memory
Memory Side Processing
Migrating
Thread
Multi-Threaded
Core(s)
Accelerator
Core(s)
Network
Interface:
H/W
Transport
Thread States
Spawn
Interface
Accelerator
Core(s)
Accelerator
Core(s)
No coherency traffic
Very fast atomics
No S/W stack for comm
H/W supported spawns
Thread
States
Near-Memory
Operations
See “Preparing for Future Heterogeneous Systems Using Migrating Threads”, ExHET Workshop, PPOPP, Edinburg, Scotland, March 2, 2024

## Slide 63: “Zettascale” in 2036?
Zettascale HPL (1021 64b flops/s) not feasible
  64bit FPU might go from today’s 10pJ to 2-3pJ
  Just math path of ZettaFLOPS HPL machine would consume 2-3GW
Better: 1000X for today’s critical apps in same footprint
  Multi-physics esp. Climate modeling; Molecular dynamics; …
  Machine Learning; Bioinformatics; …
Non-starter: Technology scaling
  Effective gate lengths may drop 3+X to 1-2nm
  But metal pitch unlikely to improve significantly
  3D stacking might give 8X, but costly & little energy improvement

## Slide 64: Bridges to Zettascale
Efficiency via Specialization
  Reduced precision & specialized data types & operators
  Memory system specialized to minimize data movement
    E.g. 15,000X for bioinformatics accelerator
Reduce design costs via chiplets
  Design just the accelerator core, not the whole system
Growth of AI into Scientific Computation
  Orders of magnitude improvement on some problems
Explicit Support for Sparsity
  Fine grain memory to avoid overfetch
  Finer-grained transfer on networks for better small-message traffic
  Efficient scatter/gather, pointer walkers

## Slide 65: Conclusions
Petaflops to Exaflops took longer than expected
  But architecture remarkedly close to 2008 Exascale Report
2008 Study nailed need for SIMD many-core, stacked memory, networks based on high radix switches
But 2013 technology was insufficient
  Too many endpoints, too much power lost to movement
Frontier leveraged better technology
  With wider SIMD, multi-die packaging, better networks & cooling
More nuanced answer to “Did Frontier achieve exascale goals?”
  Yes if flop-intensive
  No if memory or bandwidth-intensive