## Slide 1: Reliable Novel Compute Methods for Unreliable Environments
Presenter: George Michelogiannakis
Applied Math and Computational Research Division (AMCR), LBNL
mihelog@lbl.gov

## Slide 2: HPC’s Future If We Do Not Change Course
“Business as usual” is not sustainable
Credit: John Shalf, LBNL
Notes: HPC performance development according to Linpack. The vertical axis is the factor of performance improvement for the sum of all systems on the Top500 list as measured by the Linpack benchmark. Whereas performance improved by a factor of 1000x every 11 years for the first 2 decades of the Top500, this figure has dropped precipitously in the past decade.

## Slide 3: Today’s Topics
Superconducting digital computing
Reliable computation on unreliable hardware and environments
  (at room temperature)

## Slide 4: Superconducting Digital Computing

## Slide 5: Move Compute Closer to Cryogenic Sensors/Qubits
Expensive and noise-prone cables to move data to room temperature
Lower temperature environments are more noisy

## Slide 6: Challenges
Device density
  Makes area a primary constraint
  And memory capacity
Cables to room temperature
Reliability under harsh environments
  Or with cooling and device variations
I Nagaoka et al., “A 48GHz 5.6mW Gate-Level-Pipelined Multiplier Using
Single-Flux Quantum Logic”, ISSCC 2019
P Pintus et al., “Ultralow voltage, high-speed, and energy-efficient cryogenic electro-optic modulator”, Optica Vol. 9, Issue 10, pp. 1176-1182 (2022)

## Slide 7: Data Encoding in Race Logic
Epochs repeat
Epoch duration = TimeSlotDuration NumTimeSlots
Each pulse represents an equivalent 2N binary number (N = NumTimeSlots)
Can efficiently represent non power of two number ranges
An epoch contains N time slots. A pulse in time slot “I” encodes the value “I”
G Tzimpragos et al., “A computational temporal logic for superconducting accelerators”, ASPLOS 2020
Time
Epoch
0
1
2
3
4
Num = 1
Num = 4

## Slide 8: Instead: Unipolar and Bipolar Race Logic
Changing the range of representation to [0,1] (unipolar)
or [-1,1] (bipolar)
To obtain bipolar representation
P Gonzalez-Guerrero et al., “Temporal and SFQ pulse-streams encoding for area-efficient
superconducting accelerators”, ASPLOS 2022
Time epoch
Slot
1
2
3
4
5
6
7
8
RL
A = 3
0.125
0.25
0.375
0.5
0.625
0.75
0.875
1
Unipolar RL
A = 3/8
0 to 1
-0.75
-0.5
-0.25
0
0.25
0.5
0.75
1
Bipolar RL
A = -0.25
-1 to 1

## Slide 9: Pulse Train Operands
Maps a value to the number of pulses. “1” is for the maximum number of pulses
To obtain bipolar representation
(not shown)
P Gonzalez-Guerrero et al., “Temporal and SFQ pulse-streams encoding for area-efficient
superconducting accelerators”, ASPLOS 2022

## Slide 10: U-SFQ: Race Logic and Pulse Stream Operands
This shows a multiplication. The output is a pulse train
P Gonzalez-Guerrero et al., “Temporal and SFQ pulse-streams encoding for area-efficient
superconducting accelerators”, ASPLOS 2022

## Slide 11: What is Keeping us Away From mK?
Such as 300 mK

## Slide 12: Power Limits
Simple 16-bit adder. Results with qPalace. 50% activity factor in every input
https://github.com/andreamurillomtz/decimation_filter.git
~1000x gap with μW target
How to reduce power?
ERSFQ/eSFQ (static power)
Fewer gates (smaller circuit)
Lower activity factor
Lower clock frequency
10mW active power
Notes: 1118 gates

## Slide 13: U-SFQ’s Power Requirements
Power depends on numerical value of inputs. Higher numbers -> more pulses
P Gonzalez-Guerrero et al., “Temporal and SFQ pulse-streams encoding for area-efficient
superconducting accelerators”, ASPLOS 2022
Active power consumption for the bipolar multiplier, using three different pulse
streams frequencies representing the numbers −1, 1, and 0. We vary the RL input from -1 to 1.
RSFQ. RL and pulse train inputs set to half the maximum value
32-input 8-bit U-SFQ dot-product unit

## Slide 14: Noise / Variability
SFQ devices are usually biased around 70% of their switching voltage
If noise levels are high, fluctuations in voltage can cause JJs to produce erroneous pulses
  SFQ devices due to their low switching energy and particularly susceptible
Noisy grounds and power supplies can cause issues with device performance
These are already challenges in 4K, worse at 300mK
  SFQ devices need to be tuned
Can compute models accept device errors but bound the numerical error?
We need a solid noise model and resulting simulation models
From external factors, cooling imperfections, and device variability
0
1
2
3
4
Erroneous pulse appears
Notes: Best paper I can find: https://iopscience.iop.org/article/10.1088/1742-6596/97/1/012041/pdf
How to calculate BER of a given RSFQ cell: https://ieeexplore.ieee.org/document/1211653
Electromagnetic shielding is important. SFQ circuits are susceptible to trapped flux, leading to inconsistent pulse generation. A double layer cryoperm shield is used to ensure the device is operating in a low field environment. A superconducting aluminium shield can also be used to protect the chip from stray or residual fields.
Shielding on the wiring has also been seem to be key. Metallic braiding is needed around all of the dc ribbons, both inside and outside the cryostat. Individually shielded twisted pairs are also being integrated into the system to reduce crosstalk / noise. Non-magnetic components must be used throughout the system, particularly around wire connections and device mount.

## Slide 15: How Do Compute Models Affect Error?
For binary, pulse trains, and race logic:
  How does an erroneous pulse appearing affect the represented value?
  How about a pulse disappearing?
  How about a pulse shifting?
Predictability of errors matters too, not just its numerical impact
Binary
Erroneous pulse
Pulse shift: no numerical effect
Pulse disappear or appear: Small and bounded error
Pulse shift: Small error
Pulse disappear: Zero!
Pulse appear: No error or lower value

## Slide 16: Reliable Computation on Unreliable Devices and Environments

## Slide 17: Reliable Distributed Computing With Unreliable Hardware in Unreliable Environments
5G network management
LBL
5G
5G
LTE
WiFi
LoRa
STARLINK
Notes: These pictures are from sites in Alaska and Colorado that detect environmental changes and landslides. Other applications include radiation detection.
Reliability of the distributed computation is key. But also to reduce data movement from sensors to the system.

## Slide 18: Landslide Monitoring
Map of the study site showing the measured and interpolated moisture content (diamond symbols and blue shades) and the measured deformation at a subset of the monitored locations (white to red dots)
Geophysical sensors to derive a predictive understanding
Sensor density of more than 175 sensors per square kilometer
“Predictive monitoring of urban slope instabilities using geophysics and wireless sensor networks”, The Leading Edge. 2023;42(9):634-643

## Slide 19: Reliable AI in an Unreliable Environment
With many sensors, a minority of the hypervector missing will not affect final classification result, with high probability
Alternative models such as CNNs also possible but resilience has not been in focus yet
With privacy in case communication is monitored or sensors get reverse engineered
Partial hypervector
Sensor1 observation
Sensor2 observation
Sensor3 observation
Sensor4 observation
Partial hypervector
Partial hypervector
Partial hypervector
Optional hashing step
Distributed or centralized
communication step
Entire hypervector in one location. Can produce final result
Future work
Notes: Distributed CNNs: https://ieeexplore.ieee.org/document/9763736

## Slide 20: Bit Error Rate (BER) in Emerging Devices
BER depends on applied gate voltage, process variation, and temperature
  BER is affected asymmetrically for 0s and 1s with temperature
  0 to become 1 more probable
  Almost a linear relationship
At 85C and different read voltages:
  14nm FeFET, 10nm Fe layer
  0.1V
    P01 = 2.198%
    P10 = 1.090%
  0.25V
    P01 = 2.098%
    P10 = 0.190%
Ferroelectrics as an example
“FeFET-Based Binarized Neural Networks Under Temperature-Dependent Bit Errors”, IEEE Transactions on Computers, July 2022
Notes: Linear relationship of BER (separately for 0s and 1s) and temperature.
0s and 1s means the probability for a 0 to become a 1, and 1 to become a 0.
Details on Our TCAD-Based Modeling of FeFET. As earlier mentioned, in our work the entire Ferroelectric FinFET (FeFET) device is fully implemented and modeled in Technology CAD (TCAD) framework (Synopsys Sentaurus). Concisely, we model and calibrate a 14nm FinFET device using TCAD, and then the high-k layer (1.7nm) in the gate stack is replaced with a 10nm ferroelectric layer (Hf0:5Zr0:5O2) located on top of the SiO2 layer. It is noteworthy that our device modeling is not just a combination of a Ferroelectric capacitor model and a FinFET model but, in fact, the complete ferroelectric FinFET device is fully modeled in TCAD using a meta-ferroelectric-insulator-semiconductor (MFIS) stacks. For accurate modeling, the density gradient model is used to account for the quantum confinement effects and, additionally, the thinlayer mobility model is used to account for the scaled fin dimensions. The crystal orientation effects on the channel mobility, channel strain-related mobility improvement, and ballistic mobility to account for the quasi-ballistic carrier transport in such nano-scaled dimensions have also been considered. T

## Slide 21: Reliable AI Models can Mask Bit Errors
Framework based on hyperdimensional computing (HDC) and compared against a graph neural network (GNN)
  Study includes models of FeFETs as well as FeFET hardware blocks for memory, element-wise vector product, and vector-matrix product
So we can allow devices to be error prone thus more efficient
“Reliable Hyperdimensional Reasoning on Unreliable Emerging Technologies”, IEEE ICCAD, 2023
MRR: Mean reciprocal rank. X-axis on a per-thousand scale
MRR measures the average reciprocal rank of predictions, with higher scores indicating more accurate predictions ranked closer to the top
Notes: It also includes quantization of hypervector values and elements.
MRR is a crucial metric to assess graph reasoning. The mean reciprocal rank is a statistic measure for evaluating any process that produces a list of possible responses to a sample of queries, ordered by probability of correctness. The reciprocal rank of a query response is the multiplicative inverse of the rank of the first correct answer: 1 for first place, 1⁄2 for second place, 1⁄3 for third place and so on. The mean reciprocal rank is the average of the reciprocal ranks of results for a sample of queries Q.

## Slide 22: Conclusion
Questions?
Lets adapt compute models to mask unreliability, reduce area, and reduce power
This will allow more efficient compute and in domains that are impractical now

## Slide 23: Power Limits
Simple 16-bit adder. Results with qPalace. 50% activity factor in every input
https://github.com/andreamurillomtz/decimation_filter.git
~1000x gap with μW target
How to reduce power?
ERSFQ/eSFQ (static power)
Fewer gates (smaller circuit)
Lower activity factor
Lower clock frequency
10mW active power

## Slide 24: Background: Superconductivity
Resistance of mercury and other materials drops to near zero below ~4K
Gallardo et al, “Superconductivity observation in a (CuInTe 2 ) 1-x (NbTe) x alloy with x=0.5”

## Slide 25: On-Chip Data Movement Efficiency is Impressive
May cause us to re-think architectures
IEEE International Roadmap for Devices and Systems, “Cryogenic Electronics and Quantum Information Processing.”

## Slide 26
Cross-Validation
Theory / Modeling / Simulation
(Applied Math and HPC)
Experiment /Synthesis / Prototype
(Experimental Facilities)
Systems
Resource Disaggregation
Photonic Interconnects
Neuromorphic/non-Von/compute
Circuits
Automated std. cell generation
EDA/Circuit Synthesis
Superconducting Race Logic
Devices
ncFET and MESO, Superconducting
Spin-orbit magnetoelectric logic/mem
EUREKA EUV Patterning
Materials
Superconducting Materials
Ferroelectrics, Multiferroics
Robotic/automated synthesis (A-Lab)
PINE
100 Exaflops at < 20MW
A-Lab
MoSAIC
A Cross-Layer Approach With New Devices
Notes: Jackie alvarez fellow
Talk a-lab
Building these connections is harder than it looks
We view ourselves as ASCR’s mcroelectrionics lab

## Slide 27: Multiplication With Just One or Four Cells
P Gonzalez-Guerrero et al., “Temporal and SFQ pulse-streams encoding for area-efficient
superconducting accelerators”, ASPLOS 2022
Essentially a CMOS XNOR
The bipolar multiplier for stochastic computing
Before “B”, pulses in “A” pass
After “B”, the complement of “A” pass
The output is their merge
“Clk” denotes time slot boundaries
Notes: Bipolar multiplier: Before the arrival of the RL pulse B, the top NDRO lets the pulse stream A pass through. As a result, 𝑂 1 = 𝐴 ∧ 𝐵 . When B arrives, it sets the bottom NDRO letting ¬ 𝐴 pass. As a result, 𝑂 2 = ¬ 𝐴 ∧ ¬ 𝐵 . The merger combines 𝑂 1 and 𝑂 2 obtaining 𝑂 𝑈𝑇 = ( 𝐴 ∧ 𝐵 ) ∨ (¬ 𝐴 ∧ ¬ 𝐵 ).
Given two numbers $p_A$ and $p_B$ in the range of $[0,1]$, we propose to encode $p_A$ as the rate of an SFQ pulse stream A, and $p_B$ as a RL signal B. To calculate $p_A \times p_B$, we use the RL signal B to filter out a percentage of pulses from A (see Figure~\ref{fig:rl_unip}b). What remains after the filtering process, encoded in a pulse stream, is the multiplication result. To implement this, we use an NDRO cell as shown in Figure~\ref{fig:rl_unip}c (left).
Using a single NDRO, we can multiply positive numbers. That is called unipolar multiplication. To multiply negative numbers, we propose a bipolar multiplier shown in Figure~\ref{fig:rl_unip}c (right). Notice that the proposed multiplier is inspired by a CMOS XNOR, that is the bipolar multiplier for stochastic computing~\cite{gaines1967}. Before the arrival of the RL pulse B, the top NDRO lets the pulse stream A pass through. As a result, $O1=A\wedge B$. When B arrives, it sets the bottom NDRO letting $\neg A$ pass. As a result, $O2=\neg A\wedge \neg B$. The merger combines $O1$ and $O2$ obtaining $OUT = (A\wedge B) \vee (\neg A\wedge \neg B)$.

## Slide 28: Problem Statement: RL Arithmetic is Expensive
For instance, multiplying two race logic pulses
0
1
2
3
4
0
1
2
3
4
Num = 2
0
1
2
3
4
Num = 2
Num = 4

## Slide 29: What is the Motivation?
Remember that manufacturing is generations behind CMOS
IEEE International Roadmap for Devices and Systems, “Cryogenic Electronics and Quantum Information Processing.”